## Slide 1
Naila Costa, Dietrich Epp Schmidt, Erin Larson, Stephanie Shousha
Phosphorus variation in the Colorado River Watershed
Data-driven ecological synthesis summer school
Station de Biologie des Laurentides, Université de Montréal May 7, 2017

## Slide 2: DDESSS Project
Phosphorus in the Colorado River Watershed
  How does TP, TDP variability vary with stream size?
  How does TP, TDP concentration vary with differing land use?
Predictions
  Increased homogeneity in P variability with increasing stream size
  Increasing P quantity with increased anthropogenic effect

## Slide 3: Colorado River Watershed
United States watersheds divided by HUC categories
Up to 8 numbers per division
Colorado River Watershed: HUC2 = 15
HUC4 = 1501 HUC8 = 14050006 (Corral Gulch Near Rangely, CO) Drainage area: 31.8 sqm

## Slide 4: Data Management
OpenRefine
  Cleaned the two data sets (Phosphorus & Land Use Tables)
R via Jupyter
  Average of LandUse at the HUC8 scale
SQL
  Joined Phosphorus Table to Land Use Table by HUC8 unique identifier
GitHub
R via Jupyter
  Time series
  Standard deviation + means (dplyr package)
  Multiple linear regression

## Slide 5: Outliers
10 out of 5053 observations (3 sites)
4.68 to 24 mg/L
  Not biologically possible
  Unless town, treatment plant
  Google map; satellite
  Typo

## Slide 7
Notes: No seasonal variance. So we can infer that if we find a variation depending on streams, then it’s really either the streams or the land use having an effect, and not the season.
Time series: wanted to see if the P varied through time. It doesn’t (do we have a stats to support this point?).

## Slide 8
TP variability (log SD +1 by site) vs Stream Order
Notes: Regression, no significant relationship.
Interesting funneling.
STD by site.

## Slide 9
TDP variability (log SD + 1 by site) vs Stream Order

## Slide 10: Total P, multiple linear regression

## Slide 11
Notes: Multiple linear regression to see how well the different land use types explained TP. This time with

## Slide 13
Notes: Hot spot of P, makes sense bc near Rockies
Created using heat-map plugin in Qgis which both takes into account the density of points and the values of variables associated with those points.
Not a heat map for the whole watershed, just for a concentrated amount of points.
Hotter colours = hotter values

## Slide 15: GitHub

## Slide 17: Zero Answers, Infinite Questions
Spatial overlap between total phosphorus hotspots + forest cover + Rocky Mountains – possible erosion from mountains?
Stream order not correlated with P variability – is stream order the right metric?

## Slide 18: Lessons Learned
Working in terminal is a learning curve.
Many contributors in a GitHub repository – how to have good hygiene?
Need a clear data workflow from start
Understand the dataset before you begin analysis
  Take more time in discovery phase
Do research slowly – CALM DOWN.
Jupyter Notebook was nice for coding together.
SQLlite is lit AF.

## Slide 19: THANK YOU!!